Process Spec:		Cleanroom Maintenance

Materials:			Cleanroom Suit

Cleanroom Cleaner (liquid)

Reverse Osmosis Water

Tooling:			Cleanroom Vacuum System

Cleanroom Mop and Bucket

Clean Laundry Machine

HEPA Drying Cabinet

QC Data Sheet:

Process:

Cleanroom is maintained to Class 10,000 Cleanroom Standard by following the cleanroom manufacturer's recommended procedures.

- A tack-mat is installed at the entrance to the cleanroom.

- Only approved cleanroom materials (wipes, swabs, papers, etc.) are to be used within the cleanroom.

- All equipment, supplies and tooling entering the cleanroom must be cleaned prior to entry.

- The room is vacuumed daily and mopped (with cleanroom cleaner mixed with RO water) weekly to remove accumulated dust from the walls, tables and floor.

- Anyone entering the cleanroom must wear approved cleanroom garb.

- Disposable cleanroom garb is used once and then disposed of.

- Re-usable cleanroom garb is to be worn for no more than 5 working shifts and is to be hung in HEPA cabinet between shifts.

- Once per week all worn re-usable garb is to be washed in the Cleanroom Laundry Machine.

- Hang the garments to dry in the HEPA drying cabinet.