Process Spec:	Procedure for Interconnect Board Acceptance

Components:		Printed Circuit Boards

Material:			Cotton Gloves

Tooling:			Vernier Calipers

QC Data Sheet:		Materials Inspection Report: ICB's

Process:

- Every order of ICB's is to be inspected upon receipt from vendor.

- Use the form Materials Inspection Report: PCB's to complete the inspection.

- Verify that the PCB's were manufactured to our specifications.

- The inspection is to include a review of the documentation sent with the ICB's from the vendor and the Purchase Order.

- Count the quantity delivered.

- Visually inspect the PCB's for signs of damage or defect.

- Measurement and testing as necessary to determine that PCB's meet specifications (i.e. material thickness, hole sizes).