Process Spec:		Procedure for Retaining Pin Insertion

Components:		Endplate, non-readout end

Retaining Pins

Material:			Latex Gloves

Cleanroom Wipes

Ethanol

Tooling:			Retaining Pin Insertion Tool

QC Data Sheet:		Assembly Logbook

Process:

- This procedure is to be performed in the cleanroom.

- Load a pin into the tip of the insertion tool.

- Locate the pin over the endplate hole.

- Insert the pin by gently pumping the tool 3 or 4 strokes.

ATTENTION: Do not over insert the pin.

- Remove the tool and inspect the insertion. The pin should be fully inserted and straight. Remove any damaged or improperly inserted pins.

- Record competed pin insertions in the Assembly Logbook.