Process Spec:	Quality Control Procedures for ICB and Cable Assemblies

Components:		Cabled PCB's

Tooling:			High Voltage Supply

High Voltage ICB Test Jig

Electrical Continuity Meter

Capacitance Meter

Lamp with Magnifier

QC Data Sheet:		Assembly Logbook

Process:

- Visually inspect each assembled ICB for correct component placement and good solder joints. Correct all faults.

- Place each Interconnect Board on the High Voltage ICB Test Jig. Switch on the high voltage and test the ICB.

- If the ICB under test passes, move on to the next ICB.

- If the ICB under test fails, mark the failed ICB for further examination, then move on to the next ICB.

- After all the ICB’s in a cable bundle have been tested, determine the cause of any failed ICB’s and repair them.

- Retest repaired ICB’s.

- Record all work in the Assembly Logbook.