Process Spec:	Procedure For Reverse Osmosis Water System Maintenance

Equipment:		Milli-RO 30 Plus

Model #: ZFR006030	Serial #: F9MM17051D

Reverse Osmosis Water Treatment System

Millipore Corporation

Material:			Poly Filter (CDPRM1206)

Carbon Filter (CDFC01204)

RO-Pak Pretreatment Cartridge (CPROPO402)

RO Membrane Cartridge

Chlorine Treatment Tablets (ZWCL0FS0)

RO-Clean-A (ZWACID012)

RO-Clean-B (ZWBASE012)

Tooling:			slot head screwdriver, beaker

QC Data Sheet:		RO System Maintenance Logbook

### Milli-RO Plus User Manual

Process:

- Once per week, record the operating parameters in the logbook.

- Once per month, change the poly-filter and the carbon filter. After installing the new filters run the water bypassing the RO system for 2 minutes to clear the system of carbon dust.

- Once per month, perform the Chlorine Cleaning Treatment Cycle.

  - Put the machine into Standby mode

  - Open the RO port, add the tablet, & close the port.

  - Press the Autoclean button to put the machine into CL2 Mode.

  - Return to operating mode (take machine out of Standby)

- Once per month, perform the RO Clean Treatment Cycle.

  - Put the machine into Standby mode.

  - Open the RO port, add the sachet, & close the port.

  - Press the Autoclean button to put the machine into pH  Mode.

  - Return to operating mode (take machine out of Standby).